## Slide 2: Overview
Part 1 – Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2 – Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Part 3 – Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 3: Circuit Optimization
Goal: To obtain the simplest implementation for a given function
Optimization is a more formal approach to simplification that is performed using a specific procedure or algorithm
Optimization requires a cost criterion to measure the simplicity of a circuit
Two distinct cost criteria we will use:
  Literal cost (L)
  Gate input cost (G)
  Gate input cost with NOTs (GN)

## Slide 4: Literal Cost
D
Literal – a variable or it complement
Literal cost – the number of literal appearances in a Boolean expression corresponding to the logic circuit diagram
Examples:
  F = BD + A C + A L = 8
  F = BD + A C + A + AB L =
  F = (A + B)(A + D)(B + C + )( + + D) L =
  Which solution is best?
D
B
C
B
B
D
C
B
C
Notes: 2nd Literal Cost = 11
3rd Literal Cost = 10
The first solution is best

## Slide 5: Gate Input Cost
Gate input costs - the number of inputs to the gates in the implementation corresponding exactly to the given equation or equations. (G - inverters not counted, GN - inverters counted)
For SOP and POS equations, it can be found from the equation(s) by finding the sum of:
  all literal appearances
  the number of terms excluding terms consisting only of a single literal,(G) and
  optionally, the number of distinct complemented single literals (GN).
Example:
  F = BD + A C + A G = 11, GN = 14
  F = BD + A C + A + AB G = , GN =
  F = (A + )(A + D)(B + C + )( + + D) G = , GN =
  Which solution is best?
D
B
C
B
B
D
C
B
D
B
C
Notes: G = 15, GN = 18 (second value includes inverter inputs)
G = 14, GN = 17
1st solution is best

## Slide 6: Cost Criteria (continued)
Example 1:
F = A + B C +
A
B
C
F
B
C
L = 5
L (literal count) counts the AND inputs and the single literal OR input.
G = L + 2 = 7
G (gate input count) adds the remaining OR gate inputs
GN = G + 2 = 9
GN(gate input count with NOTs) adds the inverter inputs

## Slide 7: Cost Criteria (continued)
Example 2:
F = A B C +
L = 6 G = 8 GN = 11
F = (A + )( + C)( + B)
L = 6 G = 9 GN = 12
Same function and same literal cost
But first circuit has better gate input count and better gate input count with NOTs
Select it!
B
C
A
A
B
C
F
C
B
F
A
B
C
A

## Slide 8: Boolean Function Optimization
Minimizing the gate input (or literal) cost of a (a set of) Boolean equation(s) reduces circuit cost.
We choose gate input cost.
Boolean Algebra and graphical techniques are tools to minimize cost criteria values.
Some important questions:
  When do we stop trying to reduce the cost?
  Do we know when we have a minimum cost?
Treat optimum or near-optimum cost functions for two-level (SOP and POS) circuits first.
Introduce a graphical technique using Karnaugh maps (K-maps, for short)