## Slide 1: Karnaugh Maps (K-map)
A K-map is a collection of squares
The collection of squares is a graphical representation of a Boolean function
  Each square represents a minterm
  Adjacent squares differ in the value of one variable
The K-map can be viewed as
  A reorganized version of the truth table

## Slide 2: Some Uses of K-Maps
Provide a means for:
  Finding optimum or near optimum
    SOP and POS standard forms, and
  Visualizing concepts related to manipulating Boolean expressions, and
  Demonstrating concepts used by computer-aided design programs to simplify large circuits

## Slide 3: Two Variable Maps
A 2-variable Karnaugh Map:
  Note that minterm m0 and
  minterm m1 are “adjacent”
  and differ in the value of the
  variable y
  Similarly, minterm m0 and
  minterm m2 differ in the x variable.
  Also, m1 and m3 differ in the x variable as well.
  Finally, m2 and m3 differ in the value of the variable y

## Slide 4: K-Map and Truth Tables
The K-Map is just a different form of the truth table.
Example – Two variable function:
  We choose a,b,c and d from the set {0,1} to implement a particular function, F(x,y).
Function Table
K-Map
Input
Values
(x,y)
Function
Value
F(x,y)
0 0
a
0 1
b
1 0
c
1 1
d
y = 0
y = 1
x = 0
a
b
x = 1
c
d

## Slide 5: K-Map Function Representation
Example: F(x,y) = x
For function F(x,y), the two adjacent cells containing 1’s can be combined using the Minimization Theorem:
F = x
y = 0
y = 1
x = 0
0
0
x = 1
1
1
x
y
x
y
x
)
y
,
x
(
F
=
+
=

## Slide 6: K-Map Function Representation
Example: G(x,y) = x + y
For G(x,y), two pairs of adjacent cells containing 1’s can be combined using the Minimization Theorem:
G = x+y
y = 0
y = 1
x = 0
0
1
x = 1
1
1